## Slide 1
DMCA
Dynamic Model-Context Alignment
A Digital-Twin-driven framework for constraint-aware selection and re-alignment of edge AI models
Kevin Omede
M.Sc. Industrial Production and Technological Innovation Engineering — Politecnico di Torino
Dual degree with Business Administration and Production Systems — UIC Barcelona
Visiting Researcher, Beihang University
Supervisor
Prof. Alessandro Simeone
Defence
September 2026
Prepared for the joint call with
IRT SystemX & Paris-Saclay — June 18, 2026

## Slide 2
CONTEXT
A static decision in an evolving context
Today
Model selection for edge AI is largely a one-off design choice: pick a model, deploy, hope it holds.
But hardware, latency SLA, sensors and process drift keep changing. When the context moves, the chosen model silently becomes the wrong one.
Our framing
Model selection is a closed-loop alignment problem governed by the Digital Twin of the asset.
The DT (formalised as an AAS) carries the constraints; the framework continuously re-evaluates the fit between the deployed model and the operating context, and acts when the gap grows.
Hardware
CPU, RAM, accelerator
SLA
latency, memory, cost
Context
sensor / process drift
DMCA — Thesis Outline · K. Omede
2 / 14

## Slide 3
RESEARCH QUESTION
The question that drives the framework
How can a Digital Twin, formalised as an Asset Administration Shell (AAS), drive continuous selection and re-alignment of edge AI models when both asset constraints and data distributions evolve over time?
01
Selection
How to choose the right model given heterogeneous constraints?
02
Monitoring
How to detect and classify context shifts at runtime?
03
Action
When (and how) should the deployed model be replaced?
DMCA — Thesis Outline · K. Omede
3 / 14

## Slide 4
FRAMEWORK
DMCA — a five-stage closed loop
1
DT Profiling
AAS describes asset
2
Model Selection
TOPSIS multi-criteria
3
Edge Deployment
Quality gate (4 checks)
4
Drift Detection
ADWIN + decision tree
5
Re-alignment
Operator-in-the-loop
Closed loop — re-evaluation triggered when context drifts
Phase 1 (this thesis): single asset, JSON AAS Type 1, batch simulation. The five stages are implemented and validated empirically.
DMCA — Thesis Outline · K. Omede
4 / 14

## Slide 5
STAGE 1
DT Profiling — the AAS carries the constraints
What the AAS encodes
Hardware
CPU cores, RAM, accelerator class
Latency SLA
maximum tolerable inference latency
Sensor topology
channels, sampling rate, ranges
Operational range
expected nominal regimes
Cost budget
inference cost ceiling
Phase 1 implementation
AAS Type 1, serialised as JSON. Static per-asset descriptor consumed by Stage 2 at design time.
{
"asset": "jetson_orin_nx",
"hardware": {
"cpu_cores": 8,
"ram_gb": 16,
"accelerator": "ampere_gpu"
},
"sla": { "latency_ms": 500, "cost_max": 0.05 },
"sensors": [...]
}
Designed to be conformant with IEC 63278 (AAS, CDV) and ISO 23247 / ISO/IEC 30173.
DMCA — Thesis Outline · K. Omede
5 / 14

## Slide 6
STAGE 2
Multi-criteria model selection — TOPSIS
Four criteria, normalised and weighted
MAE
weight 0.5
Predictive accuracy (benefit)
Latency
weight 0.3
Inference time (cost)
Params
weight 0.1
Model size (cost)
License
weight 0.1
Open / restricted (benefit)
How it works
Each candidate model in the registry is scored against the AAS-encoded constraints. TOPSIS ranks them by relative closeness to the ideal solution.
Tie-breaking
params · license · data-availability · ONNX status
Fallback
If no admissible model exists: structured event + copilot alert.
Sensitivity analysis on α/β weights performed as ablation.
DMCA — Thesis Outline · K. Omede
6 / 14

## Slide 7
STAGES 3 & 4
Guarding the deployment, watching for drift
3
Edge Deployment — Quality Gate
Four checks before the candidate model is promoted to production:
Latency under SLA
Output shape consistency
Validity (no zero-shot collapse)
Memory headroom
On PASS, the AAS DeploymentState is written back.
4
Drift Detection — DMCA-Drift v3.1.1
Two-layer detector + AAS context enrichment:
Layer 1
ADWIN (River, δ=0.002) + secondary variance trigger
Layer 2
Decision tree over 8 hand-crafted features
Layer 3
AAS context enrichment (severity, recommended action)
7 drift classes: abrupt · gradual · incremental · variance shift · distribution shift · outlier-driven · unclassified
DMCA — Thesis Outline · K. Omede
7 / 14

## Slide 8
STAGE 5
Re-alignment — closing the loop with the operator
1
Shadow deployment
New candidate runs in parallel
2
Improvement check
Threshold gate before action
3
Operator confirm
Copilot L1/L2/L3, timeout policy
4
Atomic swap
10-tick grace + audit trail
Conversational copilot
Tier-based LLM router (Haiku / Sonnet) bridges drift evidence and operator decision. COPILOTCONFIRM policy: on timeout, reject if SIL≥2, approve if SIL<2.
DMCA — Thesis Outline · K. Omede
8 / 14

## Slide 9
RESULTS
Benchmark — eight foundation models, one decision
348×
Latency variation
across the 8 architectures
$0.30
Total compute cost
on serverless NVIDIA T4
500 ms
SLA threshold —
most accurate model fails it
The textbook case for constraint-aware selection
TimesFM reaches MAE = 0.006 on CMAPSS FD001 — the most accurate model in the registry — but its latency of 2039 ms makes it operationally unusable under a 500 ms SLA. Accuracy alone is not a deployment decision.
DMCA — Thesis Outline · K. Omede
9 / 14

## Slide 10
RESULTS
A full drift-and-recovery cycle
t = 0
Baseline operation, MAE ≈ 0.796
t = 1380
ADWIN detection (δ=0.002)
t = 1385
Drift classified, candidate selected
t = 1400
chronos-t5-tiny swapped in
after
MAE recovers to 0.174 within 20 ticks
Validation
92%
Held-out accuracy
on the 7-class drift typology, 5 seeds × 5 drift types
FAR = 0.000
No false alarms across the held-out runs.
DMCA — Thesis Outline · K. Omede
10 / 14

## Slide 11
POSITIONING
Where DMCA sits in the DT standards landscape
IEC 63278 (CDV)
AAS for industrial applications
Implementation substrate — what the AAS structure looks like in DMCA.
ISO 23247
DT framework for manufacturing
Reference architecture for the manufacturing context the framework targets.
ISO/IEC 30173
DT — concepts and terminology
Cross-domain semantic framing of the Digital Twin in the loop.
DMCA is implementation-light by design: Phase 1 keeps the AAS as JSON, leaving the runtime / distributed layer as an explicit extension point.
DMCA — Thesis Outline · K. Omede
11 / 14

## Slide 12
SAFETY CASE
The Safety Cost of Ignoring Latency
A model chosen on accuracy alone can be 6× more accurate and still unsafe — because a single violated constraint silently destroys the ability to detect drift on the edge.
Accuracy-first pick
Moirai-S
MAE
0.228
6.1× better than PatchTST
Latency on T4
53.73 ms
within benchmark budget
Projected on Jetson Nano
~537 ms
10× T4→Jetson factor
10.7× SLA violation
~6,700
checks/h
(vs. 122,900)
< 2 inferences in the 1000 ms drift window — drift NOT detected
Constraint-aware pick
PatchTST
MAE
1.303
baseline accuracy
Latency on T4
5.86 ms
highly stable P95
Margin-adjusted (×1.5)
8.8 ms
inside the 50 ms SLA
Inside SLA — admissibility PASS
122,900
checks/h
(full monitoring rate)
34 inferences in the 1000 ms drift window — drift detected.
A 6× MAE advantage becomes safety-inferior under a single violated constraint. DMCA's Stage 3 admissibility filter blocks this scenario automatically.
DMCA — Thesis Outline · K. Omede
12 / 14

## Slide 13
COLLABORATION
Where DMCA can grow — applied to something real
Architecture & integration
Application & validation
01
Distributed AAS
From a single static JSON to AAS instances across cloud / fog / edge, with submodels populated by runtime node status.
02
Selection as DT service
TOPSIS lifted from a batch script to a live service consuming submodels and emitting decisions per node.
03
Multi-asset federation
DMCA across a fleet of heterogeneous assets, with AAS-to-AAS coordination and shared model registry.
04
IRT SystemX use case
First real validation on a partner industrial case — beyond synthetic CMAPSS / ETT benchmarks.
05
AM quality control
Adapt DMCA to additive manufacturing process monitoring — tolerancing-sensitive, sensor-rich, drift-prone.
06
Operator trust study
Trust-calibration experiments with real operators in a Learning Factory environment.
Inspired by the May 2026 exchange with Dr. A. Belfadel (IRT SystemX) — open to any direction the joint discussion takes.
DMCA — Thesis Outline · K. Omede
13 / 14

## Slide 14
Thank you
Looking forward to the conversation.
Kevin Omede
kevinomede2002@gmail.com
M.Sc. candidate — Politecnico di Torino × Beihang University